Contents

qlc3d Manual

Insert a short description of what qlc3d is and does.

Reference Richard's paper Eero's thesis.
# Installation
qlc3d can be compiled for both Windows and Linux PCs. In theory it should be possible to compile it for Macs too, but this has not been tested and there are no plans to do so. Currently, only 64 bit versions exist, not 32 bit.
## Windows
On windows qlc3d is installed by running the qlc3d64_installer executable. This will prompt for an installation directory and copy the all the required files into this directory. After this, the installation directory is added to the system PATH environment variable making it possible to run the qlc3d program from any directory.
### Manual Installation
If you don't have sufficient user privileges to run the qlc3d64_installer executable (because you're for example on a shared university computer) it is still possible to manually do the installation. The installer program is a self extracting LZMA compressed archive and can be opened with e.g. the 7zip program. Just extract all the contained files to some directory that you have write privileges to and add that directory to your personal PATH environment variable (i.e. not for all users).
## Linux
Currently no Linux installer exists. Follow the instructions for manual installation on Windows. To set the PATH variable for a single user, the .bashrc file in the user's home directory can be modified by adding the following line to the end of the line:

export PATH=${PATH}:<path to qlc3d directory>

where <path to qlc3d directory>, without the '<' and '>' signs is the path to the directory containing the qlc3d executable.
## Verifying the Installation
To verify that qlc3d has been correctly installed, open a new command prompt and type

qlc3d

followed by return. If the installation was successful, qlc3d will print a short message. If not, an error message from the operating system complaining about not finding any programs by name qlc3d will be displayed instead.
## Uninstallation
It is safe to simply delete the qlc3d installation directory and remove it from the PATH environment variable. No registry keys or other system settings are modified or created during installation.
# Running qlc3d
It is recommended that qlc3d is run from the command line. The reason is because when qlc3d encounters problems, error messages that may help resolving the problem are printed on the screen. If qlc3d is started by simply double clicking on the executable, the opened window will close before there is time to read the error message.

In general, qlc3d is run by typing to the command prompt:

qlc3d <settings file name>

where <settings file name> is the name of a text file that contains the parameter values required to run the simulation. This file is called the settings file in this document, but the actual file name can be anything (e.g. “settings.txt” will do). The contents of this file are described later in this document.

In addition to the settings file, qlc3d requires a mesh file that contains the finite elements mesh for the simulated structure. Typically this file would have been made using some external mesh generator program, such as GiD. The name of the mesh file, among other things, is specified in the settings file.

## Suggested Directory Structure
It is convenient to create a single descriptively named project directory that contains a single settings file and a single mesh file. It is of course possible to keep multiple settings/mesh files in this directory (e.g. multiple related but somehow different meshes), but in general it is easier to keep unrelated simulations in separate directories. This ensures that all the files needed to run a simulation (or series of related simulations) and the result files output by qlc3d are kept well organised and together.

When qlc3d is run from the project directory, by default a result directory named “res” is created within the project directory and all the result files are written there. Multiple result directories with different names can be created by specifying this in the settings file (see the SaveDir setting). This makes it possible to run qlc3d with different parameters without overwriting previous results.

In addition to result files, qlc3d also makes copies of both the current settings and the current mesh files and places them in the result directory. This means that each result directory also contains all the input files used to generate the result files. This makes it easy to repeat a simulation or check the value of some parameter etc. at a later time (for example when writing up a final report, some months after the actual results were obtained).
# Settings Files
qlc3d is controlled by a single text file that contains all the required settings and parameters. This file is called the settings file.

Some or the parameters described below are mandatory (such as the name of the mesh file to use), but not all. When a parameter value is not defined in the settings file, “reasonable” default value is assumed for the parameter. When a parameter is defined, its value overrides the default.
The exception...
In some cases, the values of some parameters result in other (conflicting or nonsensical) parameters being ignored, even when defined. For example, when the type of an anchoring surface is defined to be “strong” (implying infinite anchoring energy strength), its (finite) strength value as defined in the settings file is ignored and does not affect the simulation.
## Settings File Format
A settings file is a simple text file that can be edited using any text editor (e.g. Notepad++ on widows or gedit/Kate/nano/vi(m) on Linux). The file contains a number of '='-sign separated key-value pair assignments:

<key> = <value>

where <key> is the name of a parameter and <value> defines its value. Capitalisation of both keys and values is ignored, so that the following are all equal:

key = value
Key = Value
KeY = VALUE

The values can be scalars, vectors/lists or text, depending on their meaning. Vector/list values start with ‘[‘and end in ‘]’, and each value is separated by a comma. In addition, anything on a line following the '#’ –character is interpreted as a comment and does not affect the simulation.

Examples of valid vector, scalar and text key/value pairs with comments:

# This is a comment
SomeVector = [1, 2, 3] # This is also a comment
SomeScalar = 1e-3
SomeText = text
SomeListOfText = [text1, text2, text3]

The settings file is not interpreted, so writing expressions including arithmetic operations results in an error and referring to other previously defined key name as a variable is treated as a key/value pair with a text value, so it is not possible to do scripting with variables in the settings file.

key1	= 2	# This is a valid assignment
key2 = 1+2	# error, arithmetic not supported
key3 = key1	# not error, but assigns text to key3
# Settings Index
Below, the possible key-value pairs are listed. These are roughly grouped by their use.
## General Settings
### MeshName
Mandatory.
Determines the filename of the finite elements mesh used. The path, if provided, is w.r.t. to the current directory where qlc3d is run from.

Example 1: the mesh file “mesh.msh” is in the current directory
MeshName = mesh.msh

Example 2: the mesh file “mesh.msh” is in a sub-directory named “meshes”
MeshName = meshes/mesh.msh
### EndCriterion
Optional (default = Iterations, TODO:check this)
Specifies what criterion is used to end a simulation. This parameter is used in conjunction with the EndValue parameter. Supported values for this parameter are:
Iterations	The simulation finishes when number of iterations or steps has reached the value specified in EndValue
Time	The simulation finishes when the simulated time is greater or equal to the value specified in EndValue
Change	The simulation finishes when the Q-tensor appears to have reached a steady state. The largest change in any of the Q-tensor components between two successive iterations or steps is monitored and the value specified for EndValue is used as the threshold for determining when steady state is reached. / When this option is used, both the current Q-tensor change and the target value are displayed on the screen at the end of each step. / Note that if the EndValue used is too small, it is possible that this criterion is never met. This can be caused e.g. due to a too coarse a mesh or something else preventing convergence.

### EndValue
Optional (default value EndValue = 5 TODO:check this).
Defines the numerical threshold value used in conjunction with the EndCriterion parameter to determine when to end a simulation. The meaning of this value depends on the value used for EndCriterion:

Example 1. Simulate for 1000 steps:
EndCriterion = Iterations
EndValue = 1000

Example 2. Simulate a 15 ms time period:
EndCriterion = Time
EndValue = 15e-3

Example3. Simulate until largest change in Q-tensor is below 6 significant digits:
EndCriterion = Change
EndValue = 1e-6

### dt
Optional (default value: dt = 1e-9)
Numerical value determining the initial time step duration in units of seconds.

qlc3d uses an adaptive time stepping scheme that automatically changes the size of the time step at each step in an attempt to maintain a constant change in the Q-tensor for each time step. That is, the size of the time step is automatically decreased when the Q-tensor varies rapidly to maintain accuracy. Similarly, the size of the time step is increased when the Q-tensor changes slowly in order to speed up the simulation. The way this algorithm works is controlled by the parameters dtLimits, TargetdQ and dtFunction.

If dt is set to zero, a steady-state solver mode (Newton-Raphson method) is used instead. This mode can be used to more quickly find a stable steady state solution, when the dynamics of the LC material are not of interest. The steady state mode may fail to converge to a solution for a number of reasons, including:

1. Initial starting condition is not good enough.
2. The mesh is not fine enough for the problem (e.g. in the presence of defects).

Hint:
It is often a good idea to first run a simulation for a short while (e.g. for one milliseconds) with dt > 0. Then using a the last result file as an initial starting LC configuration and setting dt = 0 to try to find the final steady state solution. See also the LoadQ, EndCriterion and EndValue parameters to do this.

dtLimits = [1e-09, 1e-3]
Vector of length 2, specifying the minimum and maximum values that dt can take. Adaptive time stepping will adjust the value of dt during a simulation if intial dt is not 0.

TargetdQ = 1e-3
When time-stepping (dt>0), the value of dt, is adapted after each step so that the maximum change in the Q-tensor approaches this value. I.e., if dQ > TargetdQ, dt is decreased and vice versa.

When trying to directly solve for a steady state solution using the Newton method (dt = 0), this parameter controls the degree of damping applied. The change in Q-tensor is scaled so that it is always less or equal to TargetdQ. This helps preventing the solution from diverging.

dtFunction = [0.25, 0.8, 1.2, 10]
Array of length 4. The value of dt is changed according to dt(n+1) = S(R) * dt(n), where R is the ratio R = dQ/TargetdQ, n is time-step number and S is a piecewise linear function whose extreme values are limited between 0 and 2.

dtFunction[0] = value of R where S = 0;
dtFunction[1] = minimum value of R where S = R;
dtFunction[2] = maximum value of R where S = R;
dtFunction[3] = value of R where S = 2;

Additionally, the limits set in dtLimits are enforced.

MaxError = 1.0000e-03
numerical value used as an accuracy parameter for the nonlinear Crank-Nicholson time-stepping. Newton iterations are performed within the time step until dQ is less or equal to MaxError,

numAssemblyThreads = 0
An optional numerical value, larger or equal to 0, that specifies the number of threads to use in assembling the matrix problems. The default value is 0, which results in all the available threads being used.

NumMatrixSolverThreads = 0
An optional numerical value, larger or equal to 0, that specifies the number of threads to use in solving the matrix problems. The default value is 0, which results in all the available threads being used. Note that, optimum performance is achieved using a value larger than 0 but smaller than the number of cores/hardware threads available on the system.

## Result Input/Output
Settings related to specifying result file output formats are given below.

SaveDir = name of results directory
String value determining a sub-directory where results are saved. If the directory does not exist, it will be created. If result files from previous simulations already exist in this directory, these will be overwritten. This value is empty by default, in which case results are written in the sub-directory “/res” (which is crated automatically if it does not exist).

SaveFormat = [type1, type2 … typeX]
Vector of strings specifying file format of saved result files. Possible file types are:
LCview, LCviewTXT, RegularVTK, RegularVecMat, DirStackZ. When SaveFormat is not specified the deafault is LCview.
LCView	Default save format, does not have to be explicitly specified. Saves Q-tensor and potentials into binary files, viewable using LCView program. Files written are named as: / “result<iteration number>.dat” and “result_final.dat”
LCviewTXT	Saves director values and potential into human readable text files, also viewable using LCView. The ordering of the nodes is specified by the correponding mesh file that is also saved in the same directory. Files are named as: / “result_t<iteration number>.dat” and “result_t_final.dat”.
RegularVTK	Saves director order parameter and potential values interpolated onto a regular grid in a human readable text file. Details about this format can be easily found e.g. by googling “vtk file formats”
RegularVecMat	Saves director, order parameter and potential values interpolated onto a regular grid into text files that can be executed as scripts in MATLAB to load the values into variables.
DirStackZ	Saves director components only to a comma separated values (CSV) text file. The first line gives the number of points in x,y, and z directions as well as a time step value (in seconds). The remaining rows list the director x,y and z components. Each row corresponds to a stack of directors along the Z-axis. Within each stack, director components are interleaved (i.e. ordered nx, ny, nz, nx, ny, nz,...). Stack locations in the x-y plane increase in the x-direction first, then y direction is increment by one.
VTKUnstructuredAsciiGrid	Saves the potential values and director vector using VTK unstructured legacy grid files (ASCII text files), which also include the FE mesh at each time step. These files are comaptible for example with the ParaView data visualisation application. For details about this format see e.g. https://kitware.github.io/vtk-examples/site/VTKFileFormats/ (“Simple Legacy Formats” section)

RegularGridSize = [nX, nY, nZ]
Vector specifying the size (number of points in the x, y and z directions) of a regular, evenly spaced grid used for saving results. This must be specified., for example, when SaveFormat is set to or includes RegularVTK or DirstackZ.

The grid points are spaced evenly between the minimum and maximum coordinates in each dimension. Example:
RegularGridSize = [10,1,10] results in a 10 x 1 x 10 (2D) slice centred along mean y-coordinate of the structure.

There may be some problems with non-cuboidal structures, when regular grid points are located outside the modelling window (i.e. not in any tetrahedron). This should be a TODO item...

SaveIter = integer value
Numerical value controlling the frequency, in number of iterations, of saving intermediate result files. Values larger or equal to 0 are currently supported. When SaveIter is 0, only initial LC configuration and final result are saved. Otherwise results are saved if the modulus of current iteration and SaveIter equals zero. Default value is 0.

SaveTime = real value
Numerical value controlling the frequency in seconds of saving intermediate results.
For example, SaveTime = 1e-6 , results in a result file being saved every 1e-6 seconds. The value is expected to be larger or equal than 0. Default is 0, resulting in this option being ignored.

IGNORE THIS OPTION
OutputFormat = 0
Numerical value controlling format of output file. 0 → binary files (smaller and faster) and 1 → text files. Optional, default value is 0.

OutputEnergy = 1
Numerical value determining whether LC free energy is calculated and saved in a separate matlab compatible text file (“energy.m”). 0 → no energy calculation , 1 -> energy is calculated. Optional, default = 0

StretchVector = [1.000000, 1.000000, 1.000000]
A vector of 3 specifying a three dimensional scaling of the finite element mesh. All mesh node coordinates are multiplied by their corresponding StretchVector components. Optional, default = [1.0, 1.0, 1.0]. This option can be used to scale and stretch mesh files (although stretching a mesh in one direction more than other may reduce the mesh quality).

LoadQ = result_final.dat
A string variable specifying the filename of a previous result. The Q-tensor distribution is loaded from this file and used as a starting condition for a new simulation. Optional.

## Liquid Crystal Material Parameters

Liquid Crystal Material parameters are defined using the key/value pairs specified below:

Splay, twist and bend elastic coefficients:
K11 = 1.0000e-11
K22 = 1.0000e-11
K33 = 1.0000e-11
Chiral pitch length:
p0 = 0.0e-6
This is a optional parameter. If not assigned (or assigned 0), no chirality is assumed.

Thermotropic coefficients:
A = -1.2000e+05
B = -2.1333e+06
C = 1.7333e+06

Relative dielectric permittivities parallel and perpendicular to the director:
eps_par = 18.5000
eps_per = 7.0000
Flexoelectric splay and bend coefficients (which sign convention?):
e1 = 0.0000e+00
e3 = 0.0000e+00
These are optional coefficients. If not assigned (or assigned 0), no flexoelectricity is assumed.

Rotational viscosity:
gamma1 = 0.0777

## Initial LC Orientation
Initial liquid crystal orientation is set using a number of ‘BOX’ structures ranging from BOX1 to BOX99. Each box represents a separate cuboidal 3D volume whose position and size need to be specified. If box volumes are overlapping, the box with a higher number overrides the conditions of a lower numbered box within the overlapping region.

Use of Boxes is optional. When no Boxes are defined, or in regions not covered by any Boxes, a uniform LC orientation along the x-axis (no tilt, no twist) is used instead.

BOXn.Type
Type is a string variable that defines the variation of LC within the box. Currently Type can be Normal, Random, Hedgehog.
- Normal set the director in a uniform/linearly varying orientation (variation only a function of the z-direction)
- Random sets a randomized director orientation within the box.
- Hedgehog creates a +1 hedgehog defect at the centre of the box.

A Type must be defined bot the n'th BOX in order for the box to be valid. If no Type is defined, the rest of the parameters for the n'th BOX are ignored.

BOXn.X, BOXn.Y, BOXn.Z
The size and location of each box is defined by the vectors X, Y and Z (of length 2, each) that range from min to max range. It is OK if the x, y, z ranges are larger than the modelled structure; the non-overlapping regions are ignored.

BOXn.Tilt, BOXn.Twist (only used when Type is Normal)
Tilt and Twist are vector variables of length 2. Tilt[1] and Twist[1] contain the tilt and twist angles at Z[1], whereas Tilt[2] and Twist[2] contain the total variations of tilt and twist within the box in the z-direction . The default values of both Tilt and Twist are [0, 0], i.e. uniform LC director along the x-axis.

Params is a vector with additional parameters, currently not used for anything. Can be ignored. Default value is [0]

BOX1.Type = Normal / BOX1.Params = [1, 0] / BOX1.X = [0.0, 1.0] # a box from x = 0 to 1 / BOX1.Y = [0.0, 2.0] # y = 0 to 2 / BOX1.Z = [0.0, 5.0] # z = 0 to 5 / BOX1.Tilt = [2.0, 0.0] # tilt angle is uniform 2 degrees / BOX1.Twist = [45.0, 90.0] # twist varies from 45 / # to 134 degrees along the z-axis

Table 1Example of specifying an initial LC orientation region. A box of Normal type, ranging from x=0, y=0, z=0 to x=1.0, y=2.0, z=5.0 microns is defined. The tilt angle is set to 2 degrees throughout the whole of the box. The tilt angle is 45 degrees at the bottom of the box (z=0) and changes linearly by 90 degrees throughout the box, so that at the top (z=5), it is135 degrees.
## Anchoring
Liquid crystal alignment or anchoring is set using a number of FIXLC structures ranging from FIXLC1 to FIXLC99, as defined in the mesh.

FIXLCn.Anchoring
Anchoring is a string that describes the type of anchoring. Possible values are Homeotropic, Strong, Weak, Degenerate, Freeze or Polymerise.
FIXLCi.Anchoring	Description
Strong	Fixes the LC orientation to the easy direction.
Weak	Weak anchoring (strength determined by the FIXLCn.Strength parameter) in the easy direction.
Homeotropic	Fixes the LC along the local surface normal.
Degenerate	The LC is free to rotate in the local surface plane. If the FIXLCn.Strength is < 0, this becomes weak Homeotropic anchoring.
Freeze	Fixes the LC to its initial orientation. Can be used e.g. to create non-uniform alignment.
Polymerise	Special unofficial secret feature that does not require an alignment surface in the mesh! Fixes the value of the Q-tensor at any nodes where the order parameter value is equal or below the value specified in FIXLCn.Strength.
ManualNodes	Use the FIXLCn.Params vector to manually specify mesh node numbers where to strongly fix the LC orientation to a given easy direction. You may have to look up the node numbering in the mesh file. / Note: numbering starts at 0 (whereas in mesh file it starts at 1, so subtract one), and in meshes with dielectric volume regions, node numbering is reordered in qlc3d so that all LC nodes come before dielectric nodes. This means that it is safer to look up node numbering from a previously written result mesh file than from one written by GiD when dielectrics are present.

FIXLCn.Strength
Strength is a numeric variable that defines the Rapini-Papoular Anchoring strength when Weak or Degenerate anchoring is used. If Strength is set to a negative value and Type is Degenerate, a weak homeotropic anchoring with strength |Strength| is achieved.

FIXLCn.Easy
Easy is a numeric vector of length 3. It sets the easy tilt, twist and rotation angles of the anchoring. The rotation angle is ignored for all cases except when Anchoring is Weak and K1 is not equal to K2.

FIXLCn.K1, FIXLCn.K2
K1 and K2 are optional numeric values that can be used with Anchoring = Weak to specify anisotropic anchoring strengths. The actual polar and azimuthal anchoring strengths are Strength*K1 and Strength*K2 respectively. Default values are 1 for both, resulting in isotropic anchoring.

FIXLCn.Params = [ list of numbers ]
A list of additional options can be provided to different anchoring types. The meaning of the values will depend on the corresponding anchoring type.

When FIXLCn.Anchoring = ManualNodes, the Params are mesh node indexes. In other cases this is ignored and not needed.

FIXLC1.Anchoring = Homeotropic / FIXLC1.Strength = 1e-4 / FIXLC1.Easy = [80.0000, 45.0000, 0.0000] / FIXLC1.K1 = 1.0000 / FIXLC1.K2 = 1.0000

Table 2 Example of specifying anchoring conditions. The anchoring on FixLC1 surface is set to strong homeotropic (perpendicular to the surface plane). In this case, the parameters Strength, Easy , K1 and K2 are ignored, since homeotropic anchoring type overrides these settings.
## Electric Potentials
The potentials on electrodes are defined using a number of data structures ranging from E1 to E99. Each structure corresponds to an electrode as defined in the mesh.

En.Time
Time is a numerical vector. Each value in Time[i] corresponds to a switching of potential Pot[i] on the electrodes. Note, the length of Time should be equal to the length of Pot.

En.Pot
Pot is a numerical vector of length n. Each value in Pot[i] corresponds to a potential switching at time Time[i]. Note, the length of Pot should be equal to the length of Time.

E1.Time = [0.0, 1e-3] / E1.Pot = [3.0, 0.0]

Table 3 Exampe of defining electrode potentials. Electrode 1 is switched to 3 V at time 0ms and to 0V at 1ms.
## Uniform Electric Fields
A uniform electric field may be defined by setting the x,y and z-components of the EField vector. The units of the vector are V/μm. For example, the following defines a constant field of 1.3 V / μm throughout the structure.

EField = [0 , 0 , 1.3]
Uniform electric fields can be defined in structures that do not contain any electrodes. Uniform electric fields are not functions of time, i.e. swithing on/off during a simulation is not currently supported.

What should happen when both electrodes and a uniform E-Field have been defined? Clearly we can't have both at the same time!
## Dielectric Properties
eps_dielectric = [1.0,5.0]
eps_dielectric is a numerical vector that holds the relative permittivity values of dielectric regions defined in the structure.
## Mesh Adaptation [VERSION 2]
Mesh adaptation is controlled by specifying REFINEMENT objects (see section REFINEMENT Objects), and the instances in time and/or iterations (see section Periodically Repeating Mesh Adaptation) when mesh adaptation occurs.

### Periodically Repeating Mesh Adaptation
The frequency of repeated mesh adaptation is specified by assigning a value to either variable RefRefIter or RepRefTime:

RepRefIter = iteration number
or
RepRefTime = time period [milliseconds]. # not working!!

If RepRefIter/RepRefTime are not specified, or if they are both set to a zero value, the mesh is not adapted periodically. However, it is still possible to specify explicit iteration/time instances to do this in the individual REFINEMENT objects.

Note that if a REFINEMENT object specifies iteration numbers or instances in time, these will take precedence over RepRefIter/RepRefTime for the corresponding REFINMENT object.

### REFINEMENT Objects
REFINEMENT objects are used to specify different properties (method, region, etc.) of mesh adaptation. Currently up to 99 REFINEMENT objects are supported. The following format is used:
REFINEMENTi.<key> = <value>
Where i is a number in the range 1-99, specifying the REFINEMENT object number, <key> is a property name string and <value> is the corresponding value (string, number or array).

The following key-value pairs can be defined:
Key	Value Type	Description
Type	String	Sets the type of the corresponding REFINEMENT object. This will define how the other key/value pairs are interpreted for this object. See examples below for possible values.
Values	Array of numbers	Interpretation depends on Type. See Examples below.
Iterations	Array of numbers	Explicit Iteration numbers when adaptation described by this object is performed.
Times	Array of numbers	Explicit times when adaptation described by this object is performed.
X	Array of numbers	Array of x-coordinates
Y	Array of numbers	Array of y-coordinates
Z	Array of numbers	Array of z-coordinates

REFINEMENTi.Type= Sphere
Selects elements within a spherical region centred on X, Y and Z. The Values array contains the radius/radii of the region(s). For example:

REFINEMENT1.Type = Sphere
REFINEMENT1.Values = [0.5, 0.25, 0.1]
REFINEMENT1.X = [0.5]
REFINEMENT1.Y = [0.5]
REFINEMENT1.Z = [0.5]

Performs three refinement iterations, selecting elements at 0.5, 0.25 and 0.1 micron distances from coordinate 0.5, 0.5, 0.5. (Three concentric spherical regions are selected)

REFINEMENTi.Type=Box
Selects elements within cuboidal regions specified in the X, Y and Z arrays.
Example:
REFINEMENT1.Type = Box
REFINEMENT1.X = [0, 0.1, 0, 0.05]
REFINEMENT1.Y = [0, 0.1, 0, 0.05]
REFINEMENT1.Z = [0, 0.1, 0, 0.05]
Performs two refinement iterations, selecting elements within the two cubes rangin from x, y, z = 0 to 0.1 microns for the first cube and x,y,z = 0 to 0.05 microns for the second one (the second cube is inside the first one in this casd).

REFINEMENTi.Type = Change
Selects elements in which any of the five Q-tensor components change is equal or larger than specified in the Values array. For Example:

REFINEMENT1.Type = Change
REFINEMENT1.Values = [0.2, 0.2 ]

Performs two refinement iterations, selecting any elements within which the Q-tensor change exceeds 0.2.
## Mesh Refinement OBSOLETE IGNORE THIS SECTION
Three different types of mesh refinement are supported:
1. Pre-refinement
2. Adaptive refinement
3. End-refinement
Pre-refinement
In pre-refinement, some locations of the structure are chosen and refined before the start of a simulation. The mesh is not changed during the simulation unless specified to do so using ‘adaptive refinement’. This is convenient when it is known beforehand that higher accuracy is needed in some predetermined regions of the mesh.

Adaptive refinement
In the case of adaptive refinement, the user specifies some criteria according to which the mesh is adapted during a simulation. This is useful, e.g. when defects that move about exist in the LC director field. The adaptive mesh refinement can then be set to “track” the locations of the defects and refine the mesh as needed.

End-refinement
End-refinement is performed after a simulation is finished. That is, after the EndCriterion set earlier has been satisfied. The advantage of this is that often when seeking a final director configuration (i.e. not interested in the dynamics), it is quicker to first obtain an approximate solution on a coarse mesh, refine it, and continue.
### Pre-refinement
Pre-refinement is defined in the settings file using the REFREGn structure, where n is a number ranging from 1 to 99. The REFREG structures select and define various geometric regions in the mesh where refinement is performed.

The REFREG structure consists of the following fields:
REFREGn.Type
The type field is a string that determines the shape of the refined region. Possible values are:
Sphere

REFREGn.X
This is an array of X-coordinates.
REFREGn.Y
This is an array of Y-coordinates.
REFREGn.Z
This is an array of Z-coordinates.
REFREGn.Distance
This is an array of numbers that determine the size of the refinement region. The length of this array determines the number of refinement iterations.
REFREG1.Type = Sphere / REFREG1.X = [1.0] / REFREX1.Y = [1.2] / REFREG1.Z = [1.0] / REFREG1.Distance = [0.5, 0.25, 0.125]

Table 1 REFREG example
Table 2 l Example of defining a pre-refinement region. A spherical region centred at xyz=[1.0,1.2,1.0] is defined. Three refinement iterations are performed. Elements at distances of 0.5, 0.25 and 0.125 microns from the centre of the sphere are refined. This results in three different levels of refinement, with the mesh density increasing in three steps towards the centre of the defined sphere.

### Adaptive Refinement OBSOLETE IGNORE THIS SECTION

Adaptive refinement is performed periodically during a simulation. This is not working at the moment.

AUTOREFn.Type
This determines selection criterion to use when choosing refinement region.
Currently only use: Change
AUTOREF.MaxValue
This a list of values used in choosing refinement regions. The number of values in the list specifies the maximum times refinement is performed.
AUTOREF.MinSize
An element whose size is smaller than this value will not be refined.
AUTOREF.RefIter
This specifies the frequency at which refinement is performed. So, for example, if Refiter is set to 10, adaptive mesh refinement is performed every 10’th iteration.

AUTOREF1.Type = Change / AUTOREF1.MaxValue = [value1, value2, …,valuen] / AUTOREF1.MinSize = value / AUTOREF1.RefIter = I # refinement is performed every i'th iteration

Table 1 AUTOREF example

### End-Refinement OBSOLETE IGNORE THIS SECTION
End-refinement is performed at the end of a simulation. Using the new mesh, the simulation is repeated continuing from the previous result.

End-refinement checks whether the current solution satisfies the given error criteria:
  - If yes, the program quits without further refinement.
  - If no, the mesh is refined, and the EndCriterion is modified to run the simulation again.

End-refinement is controlled by setting the fields of the ENDREF structure. ENDREF consists of the same fields as AUTOREF, but with the difference that the RefIter field determines the maximum number of times that End-Refinement is performed. This is necessary to prevent the program from running forever, which happens with certain combinations of ENDREF.Type and ENDREF. MaxValue variables.

ENDREF1.Type = Change / ENDREF1.MaxValue = [value1, value2, …,valuen] / ENDREF1.MinSize = value / ENDREF1.RefIter =I # End-refinement is performed at most I times.

Table 2 ENDREF example

//
NEW SETTINGS MOVED FROM SOLVER FILE
QmatrixSolver = Auto || PCG || GMRES

NumAssemblyThreads = integer
NumMatrixSolverThreads = integer
# Solver Settings File

This file is nolonger required. The same settings can be set in the settings file.

The “solver.qfg” file located in the same directory with the qlc3d executable contains settings for controlling various aspects of the solution process.

- nThreads specifies number of parallel threads used in the matrix assembly. Parallel solver has not been implemented.
- Q_Solver specifies solver method used for solving the Q-tensor equations.
- V_Solver specifies solver method used for solving the potential equations.

In general, the equations for the Q-tensor and the electric potential are solved using either the Preconditioned Conjugate Gradient (PCG) or the Gerneralised Minimal Residual (GMRES) method. Set Q_Solver and V_Solver to either 1 or 0.
Both PCG and GMRES require a preconditioner matrix that can be diagonal, incomplete cholesky or incomplete LU decomposition. Se the Q and V preconditioner variables to 1, 2, or 3. A maximum number of iterations and required accuracy must also be defined for both methods.
Usually the PCG method with diagonal preconditioning is fastest, but in some cases does not converge to a solution. The GMRES method with e.g. incomplete LU preconditioning is more robust, but a bit slower and uses more memory. For example, structures with Neumann boundary conditions require using the GMRES method for the potential solution since the matrix problem is non-symmetric. (detection of cases like this should really be automatic…)
The dynamics of the Q-tensor involves multiple sub-iterations per time step. If the size of the time step is too large, these sub-iterations may not converge. The Q_Newton_Panic_Iter determines the maximum number of sub iterations before the time step is scaled by the value of Q_Newton_Panic_Coeff.

nThreads = 4 / Q_Solver = 1 # 0 = PCG, 1 = GMRES / V_Solver = 1 # 0 = PCG, 1 = GMRES / #-------------------------------------------------------- / # Q-Tensor solver settings / #-------------------------------------------------------- / Q_Newton_Panic_Iter = 10 / Q_Newton_Panic_Coeff = 0.1 / # Preconditioned Conjugate Gradient Q-tensor solver settings / Q_PCG_Preconditioner = 0 # 0 = Diagonal / # 1 = Incomplete Cholesky / # 2 = Incoplete LU / Q_PCG_Maxiter = 2000 / Q_PCG_Toler = 1e-3 / # GMRES Q-tensor solver settings / Q_GMRES_Preconditioner = 2 # 0 = Diagonal / # 1 = Incomplete Cholesky / # 2 = Incoplete LU / Q_GMRES_Maxiter = 200 / Q_GMRES_Restart = 100 / Q_GMRES_Toler = 1e-3 / #------------------------------------------------------- / # Potential solver settings / #------------------------------------------------------- / # Preconditioned Conjugate Gradient potential solver settings / V_PCG_Preconditioner = 0 # 0 = Diagonal / # 1 = Incomplete Cholesky / # 2 = Incomplete LU / V_PCG_Maxiter = 2000 / V_PCG_Toler = 1e-6 / # GMRES potential solver settings / V_GMRES_Preconditioner = 2 # 0 = Diagonal / # 1 = Incomplete Cholesky / # 2 = Incoplete LU / V_GMRES_Maxiter = 2000 / V_GMRES_Restart = 50; / V_GMRES_Toler = 1e-6; / };

Table 4 Example solver.qfg file.

# Settings File Example
Below, an example settings file is given. You can copy/paste it to a text file and use it as a starting point in your own projects.
meshName = mesh3df.txt / # Simulate 10 milliseconds / EndCriterion = Time / EndValue = 10e-3 / dt = 1e-9 #dt>0 for time stepping, dt=0 for Newton method / dtLimits = [1e-9, 1e-4] # min, max allowed dt / MaxError = 1e-5 # time step accuracy / TargetdQ = 1e-2 # predictor-corrector param. / DtFunction = [0.25, 0.8, 1.2, 10]; / Savedir = results_directory # results are saved here / SaveIter = 5 # write result to file every 5 iterations / K11 = 6.2e-12 # LC elastic coefficients / K22 = 3.9e-12 / K33 = 8.2e-12 / p0 = 2.0e-6 # no chiral doping / A = -0.240000e6 # -2 degrees / B = -2.133300e6 / C = 1.733300e6 / eps_par = 18.5; # LC dielectric coefficients / eps_per = 7.0; / gamma1 = 0.0777; # LC rotational viscosity / # set initial LC orientation to 10 degrees tilt everywhere / bOX1.Type = Normal / BOX1.Params = [1,0] / BOX1.X = [0.0, 50] / BOX1.Y = [0.0, 50] / BOX1.Z = [0, 1] / BOX1.Tilt = [10,0] / BOX1.Twist = [0,0] / # FIXLC1 surface at 10 degrees tilt, strong anchoring / FIXLC1.anchoring =strong / FIXLC1.Strength = 1e-4 / FIXLC1.K1 = 1.0 / FIXLC1.K2 = 1.0 / FIXLC1.Easy = [10, 0,0] / # FIXLC2 surface at 1 degree tilt, 90 degrees twist / FIXLC2.anchoring =strong / FIXLC2.Strength = 1e-4 / FIXLC2.K1 = 1.0 / FIXLC2.K2 = 1.0 / FIXLC2.Easy = [1.0, 90,0] / # specify potentials for two electrodes / E1.Time = [0] / E1.Pot = [0] / E2.Time = [0, 5e-3] / E2.Pot = [5, 0] / # mesh contains 2 different dielectric regions. / # Set their permittivities to 4 and 5 / eps_dielectric = [4, 5]; / # Do mesh refinement every 30 iterations / RepRefIter = 30 / #split elements where Q changes by more than 0.1 per element. / REFINEMENT1.Type = Change / REFINEMENT1.Values = [0.1, 0.1] # Q change threshold / REFINEMENT1.X = [0, 1, 0, 0.2] / REFINEMENT1.Y = [0, 1, 0, 1] / REFINEMENT1.Z = [0, 10, 0, 0.5]

# Minimal Mesh File Example
Below a minimal mesh file is shown. If your mesh file looks like gibberish when opened in a text editor, you have saved it in binary format and qlc3d will not be able to read it. To save in text format in GiD, a mesh must be exported, not saved.

- The below mesh consists of 9 nodes in range 0 to 1 microns (section “Coordinates”).
- It has 12 tetrahedral elements (first section “Elements”), all of LC material (material number 4).
- It has periodic surfaces consisting of 6 x prism elements (second section “Elements”).
- It has 12 triangular elements (third section “Elements”) of material number 3 (periodic).
- The mesh does not have any alignment surfaces nor electrodes, i.e. it is a fully periodic box of LC material.
MESH dimension 3 ElemType Tetrahedra Nnode 4 / Coordinates / 1 1 0 1 / 2 0.499998865 0.500003276 0.499995589 / 3 1 1 1 / 4 0 0 1 / 5 1 0 0 / 6 1 1 0 / 7 0 0 0 / 8 0 1 1 / 9 0 1 0 / end coordinates / Elements / 1 9 8 4 2 4 / 2 4 3 1 2 4 / 3 4 8 3 2 4 / 4 5 1 6 2 4 / 5 7 4 1 2 4 / 6 9 4 7 2 4 / 7 6 9 7 2 4 / 8 5 6 7 2 4 / 9 7 1 5 2 4 / 10 1 3 6 2 4 / 11 3 8 9 2 4 / 12 6 3 9 2 4 / END ELEMENTS / MESH dimension 3 ElemType Prism Nnode 6 / Coordinates / end coordinates / Elements / 13 8 4 9 3 1 6 / 14 4 7 9 1 5 6 / 15 3 1 4 6 5 7 / 16 8 3 4 9 6 7 / 17 4 1 7 8 3 9 / 18 1 5 7 3 6 9 / end elements / MESH dimension 3 ElemType Triangle Nnode 3 / Coordinates / end coordinates / Elements / 19 8 4 9 3 / 20 4 7 9 3 / 21 4 1 7 3 / 22 1 5 7 3 / 23 3 6 1 3 / 24 1 6 5 3 / 25 8 9 3 3 / 26 3 9 6 3 / 27 3 1 4 3 / 28 8 3 4 3 / 29 6 7 5 3 / 30 9 7 6 3 / end elements